## Slide 1: Building a new TBDF application with Existing Modules

## Slide 2: Application definition
For any application is important to have the requirements ready.
Example application:
  In this case we are building a temperature data logger with Modbus Support.
  Temperatures have to be read at 1HZ rate from thermocouples.
  Needs to send the values through Modbus
  Needs to store the information in a TDMS file
Notes: Before starting the application is important to define what the application has to do.

## Slide 3: Check for Existing modules:
Check the Existing modules Page
Check GitHub
If we look into the page we find this 3 modules:
  Modbus Module
  Scan Engine Module : to read the channels
  TDMS module to write the data file

## Slide 4: Creating the new LabVIEW project
Project>> Create Project …
Select Simple Runtime engine
Add your real-time target and move the files created under it.

## Slide 5: Configure Modules
Open Default Configurator editor
Tools>>TBDF>> Launch Standard Configuration Editor
Add target
Add Engine
Create the tags that you will need
Add Scan Engine
Configure Scan Engine
Add Modbus Module
Configure Modbus
Add TDMS Module
Configure TMDS
Save Configuration

## Slide 6: Deploy configuration

## Slide 7: Run RT Code